## Slide 1: Microwave Temperature Profiler (MTP)
High Level Software design and Plan for integrating into ADS

## Slide 2: JPL Software
> 1 million lines of VB6 code
  VB6 is no longer supported by Microsoft
  Code written by scientist, not SE
Designed to support multiple MTP instruments and platforms
Complex algorithms that we’d like to understand better
Costly to subcontract to JPL for projects using MTP
  Hope to reduce support over time

## Slide 3: JPL Software
Sadly, MJ passed away leaving Boon Lim as JPL’s MTP expert
Boon finds MTP software as fragile as do we
Often times he “massages” data to allow MTP software to work with it rather than dive into the MTP source code

## Slide 4: JPL Software
Boon’s small part-time team is pursuing the following:
  Updates to MTP hardware and daq system
  An algorithm based on physical rather than statistical retrieval methods
    Invert radiative transfer equation; no need for a priori information (i.e., radiosondes)
    But, without a priori information, finding the Tropopause is more error prone
  A new version of the software to acquire rawinsondes (raobget)

## Slide 5: Migration “Road Map”
Plan was to work more collaboratively with Boon
Progress has been slow and challenged
  Contracts negotiations
  Boon’s “publish before share” indication (retrieval method only)
Meanwhile use of VB6 software increasingly challenged (Windows 7 updates breaking it)
We feel we should return to previous Road Map

## Slide 6: Migration “RoadMap”
Sequence of steps to bring MTP “into the fold”
Challenging owing to complexity
  Break a large problem into smaller pieces
Identify top level JPL programs
  Suggest approaches to addressing them
Describe what has been done so far

## Slide 7
JPL Software
Component
Diagram Legend
RAF Software
Component
MTP Instrument
Data File
3rd Party Software
Component

## Slide 8
“DAQ”
Command/
Control/
Acquisition
MTP Operations in Flight (JPL)
MTP Instrument
RAW MTP Data
“MTPbin”
Processing
Calibration
info
Archive Average Brightness Temps
Preliminary Retrieval Coefficients
ADS
nimbus
IWGadts
data

## Slide 9
“DAQ”
Command/
Control/
Acquisition
MTP Operations in Flight (JPL)
MTP Instrument
RAW MTP Data
“MTPbin”
Processing
Calibration
info
Archive Average Brightness Temps
Preliminary Retrieval Coefficients

## Slide 10: Temperature Retrieval Overview
Temperature Profile (current)
Brightness Temperature Measurement
Emitted Radiation
Brightness Temperature Measurement
Brightness Temperature Estimate
Temperature Profile (archived)
Temperature Profile Retrieval
Forward Radiative
Transfer Model
Solve for
Retrieval Coefficients
Retrieval Coefficients
Measurement
Retrieval
Approximate RT equation in polynomial form

## Slide 11: Retrieval Coefficients
Generated twice during projects
  Prior to project
    For real time operations
    Use RAOBs that represent expected conditions
  After project
    For final data processing
    Use RAOBs that represent actual atmosphere flown through

## Slide 12
“RAOBGet”
Pre-Flight Retrieval Coefficients Generation
ASCII RAOB Files
“RAOBMan”
Manager
Raob Templates
RAOB Resources
Subset &
Statistics
“RCCalc”
Radiative Xfer Modeling
Archive Average Brightness Temps
Preliminary Retrieval Coefficients

## Slide 13
“RAOBGet”
Post-Flight Retrieval Coefficients Generation
ASCII RAOB Files
“RAOBMan”
Manager
Raob
Templates
RAOB Resources
Subset &
Statistics
“RCCalc”
Radiative Xfer Modeling
Excel Spreadsheet
Single Binary RAOB File
“RAOBMan”
Manager
Excel File
Archive Average Brightness Temps
Retrieval Coefficients

## Slide 14
MTP Calibration and Retrieval (Post Flight)
Recorded RAW MTP Data
“MTPbin”
Processing
Calibration
info
Archive Average Brightness Temps
Retrieval Coefficients
Brightness Temperature Comparisons
Excel Spreadsheet
Window Corrections

## Slide 15
“RAOBGet”
Some integration to ADS has happened
“RAOBMan”
Manager
RAOB Resources
“RCCalc”
Radio Xfer Modeling
Retrieval Coefficients
“DAQ”
MTP Instrument
“MTPbin”
Mission Coordinator
Profile
nidas
UDP:Raw
Counts
nimbus
Ground Database
aeros
Archive Average Brightness Temps

## Slide 16
Proposed Next Step: Replicate MTPbin
Retrieval Coefficients
“DAQ”
MTP Instrument
“MTPbin”
Profile
nidas
UDP:Raw
Counts (calibration?)
nimbus
Profile
Archive Average Brightness Temps

## Slide 17: Steps to nimbus acting as MTPBin
Reverse Engineer algorithm from MTPBin
Implement Algorithm in Nimbus
Modify Aeros
  display profiles
  Curtain Plots (or another program)
Goal: generate same set of profiles given same set of Retrieval Coefficients

## Slide 18: Steps to nimbus acting as MTPBin
Will then run both the JPL and the RAF versions of “MTPBin” for projects
  Allow refinement of RAF version
  Create additional tools as needed (next slide)

## Slide 19: Steps to nimbus acting as MTPBin
Data processing analysis tools
  Quality Assessment
  Interactive (is it enough like using ncplot or aeros?)
    Generate statistics that can be displayed after a processing run
  Try to approach this from a need basis rather than replicating everything
Goal: Determine what subset of these we need to be satisfied with the profiles we’re creating

## Slide 20: Additional Work
Create a device driver/sensor class for MTP “DAQ”
Converting other programs
  Perhaps a SUPER intern could work on RaobGet and RAOBMan
  RCCalc will be nontrivial