## Slide 1: MTP Brainstorming
3/18/2015
Some slides to get us going

## Slide 2
Our instrument has a 3rd channel
Raw data is 3 vectors of Brightness temperatures w/11th &12th scan of a known
source (with and without noise diode)
“Brightness Temperature Space”

## Slide 3
Radiosonde data (with temperature structure similar to the atmosphere being sampled) is critical to conversion of scans from “Brightness Temperature Space” to “Temperature Profile Space”

## Slide 4
“RAOBGet”
Retrieval Coefficients Generation
ASCII RAOB Files
“RAOBMan”
Manager
Raob Templates
RAOB Resources
Subset &
Statistics
“RCCalc”
Radiative Xfer Modeling
Archive Average Brightness Temps
Preliminary Retrieval Coefficients

## Slide 5
RCCalc creates a “map” from Temperature Profile space to Brightness Temperature space (using multivariate regression) at a set of pre-defined flight levels and generates coefficients to map back
Creates one RCF (Retrieval Coefficient File) for each template
ETC.

## Slide 6
MTP Instrument
The MTP Instrument generates a scan in Brightness Temperature space
Using the Aircraft elevation and Ambient temperature, MTPBin will look through the RCF files to find the best match for the scan
The corresponding retrieval coefficients will be used to map from the scan’s Brightness Temperature space into Temperature Profile space
NOTE: Sometimes an average of two sets is used
  Weighted average of Brightness temperatures depending on flight level
  Average of two well matched RCFs

## Slide 7
MTP Calibration and Retrieval
Recorded RAW MTP Data
“MTPbin”
Processing
Calibration
info
Archive Average Brightness Temps
Retrieval Coefficients
Brightness Temperature Comparisons
Excel Spreadsheet
Window Corrections